## Slide 1: Electric Utility Industry 101
Webinar
David Schlissel
Cathy Kunkel
March 4, 2015

## Slide 2: Webinar Outline
History: regulation and deregulation
Regional electricity markets
Types of companies
How investment decisions are made
Industry trends
Components of power plant costs
Metrics for evaluating power plant performance
Where to find data

## Slide 3: History
1935: Public Utility Holding Company Act
  Restricted utility corporate structures and mergers
1990s: Restructuring of electric utility industry in some states
  Break-up of vertically integrated utilities into power generation companies, transmission companies, and distribution companies
  Only distribution companies remain under state public service commission regulation
Not all states deregulated

## Slide 4: Independent System Operators (ISOs)
Federal Energy Regulatory Commission encouraged formation of Independent System Operators and Regional Transmission Organizations (RTOs)
Ensure open access to the transmission grid, to facilitate competition
Created and manage wholesale markets for electricity

## Slide 5: Map of ISOs

## Slide 6: Electricity Markets - Energy

## Slide 7: Historical PJM Energy Market Prices
Chart: Historic power prices (PJM Western Hub)

## Slide 8: Electricity Markets - Capacity
Supposed to ensure that there are enough power plants to meet reliability goals
Forward auction to purchase capacity several years in advance
Have not provided stable price signal
Only in PJM, NYISO, ISO-NE and MISO

## Slide 9: PJM Capacity Market Prices

## Slide 10: Types of Investor-Owned Companies in the Electricity Industry
Type of Company | Function | Regulator | Examples
Merchant Generator | Owns power plants in deregulated markets | None | NRG, Dynegy
Transmission | Owns transmission lines | Federal Energy Regulatory Commission | PATH (Potomac Allegheny Transmission Highline)
Distribution | Owns distribution system | State Public Service Commission | Pepco, National Grid
Vertically Integrated Utility | Owns power plants, transmission and distribution | State Public Service Commission | Alabama Power, Northwestern Energy

## Slide 11: Utility Holding Companies
One investor-owned holding company can own a number of different subsidiaries and affiliates:
Southern Company owns:
  Regulated vertically integrated utilities
  Merchant generation
Exelon Corporation owns:
  Merchant generation
  Transmission
  Distribution
AEP and FirstEnergy each own:
  Merchant generation
  Transmission
  Distribution
  Regulated vertically integrated utilities

## Slide 12: Types of Power Plant Owners
Merchant Generation Companies
Vertically Integrated Investor Owned Utilities
Public Power utilities
Electric Membership Co-operatives (EMC)
Power agencies

## Slide 13: Investment decisions
Company Type | Factors driving investment
Merchant generators | Wholesale electricity price outlook Not interested in investing in capital- intensive generation (e.g. nuclear, coal) if prices are expected to remain low
Vertically integrated utilities | Regulatory environment and expected rate of return Want to make capital-intensive investments (new generation, pollution control equipment) to earn a rate of return through electric rates
Publicly owned utilities | Cost of debt

## Slide 14: Merrimack – Example of Benefits to IOU of Making Expensive Investments (1)

## Slide 15: Merrimack – Example of Benefits to IOU of Making Expensive Investments (2)

## Slide 16: Financial incentives driving corporate policy
Merchant generation companies:
  Interested in driving up wholesale electricity market prices
  Advocate for rule changes at ISOs
  Want to block competition from other sources, e.g. from energy efficiency and renewables
Vertically integrated companies:
  Interested in increasing sales to earn more money (rates set on a per kWh basis)
  Incentive to oppose energy efficiency and customer-owned power generation (e.g. rooftop solar)

## Slide 17: Recent Industry Trends
Opposition to energy efficiency and rooftop solar
Move back towards regulation
  Acquire regulated utilities
  Sell merchant generation business
  Transfer assets from merchant generation to regulated subsidiaries

## Slide 18: Webinar Outline
History: regulation and deregulation
Regional electricity markets
Types of companies
How investment decisions are made
Industry trends
Components of power plant costs
Metrics for evaluating power plant performance
Where to find data

## Slide 19: Components of Power Plant Costs
Capital cost is the cost of building the power plant and making periodic equipment replacements, major repairs and/or plant upgrades.
Cost of financing these capital expenditures are included in ongoing cost of generating power:
For investor-owned companies these financing costs are a blend of shareholder provided funds (equity) and borrowed money (debt).
For publicly-owned utilities and electric membership co-ops, financing costs are debt.
  General Rule -- The more it costs to build the plant, the higher the annual financing costs will be – depending on the equity and debt borrowing rates.

## Slide 20: Components of Power Plant Costs (Cont’d)
Annual depreciation expenses.
  the cost of building a power plant is amortized (spread) over the expected life of the plant. The plant owner collects this amount each year as a depreciation expense.
  For example, if it costs $1 billion to build a new fossil-fired plant with an expected depreciation life of 25 years, each year the plant owner will recover $40 million (that is, $1 billion divided by 25) through the cost of the power generated by the plant. .
Plant operating & maintenance (O&M) costs.
  Labor, materials, etc.
Fuel costs.
Cost of transmitting power from plant where it is generated to places where it is used.

## Slide 21: Fixed vs. Variable Power Plant Operating Costs
Fixed vs. variable costs.
  Financing & almost all O&M costs are ‘fixed” – have to be paid whether or not plant generates any power or how much it generates.
  Other costs, like fuel and some O&M, are ‘variable.’ These fluctuate depending on how many MWh are generated.
  Examples of variable O&M costs include costs of operating plant environmental control equipment

## Slide 22: Example of Rising Plant Construction Costs – Kemper IGCC Coal Plant - Mississippi

## Slide 23: Relative Costs Among Supply-Side and Demand-Side Resources

## Slide 24: Power Plant Cost Components – Example Prairie State Energy Campus

## Slide 25: Power Plant Metrics - Capacity & Energy
Capacity is a measure of the power that a plant can produce at any one moment or instance – measured in megawatts (MW) which are millions of watts.
  Large fossil and nuclear power plants have full power ratings in the range of 250 MW to 1500 MW.
  A large power plant will generally have several units at the same site.
Energy is a measure of how much power the plant generates over time, whether hours, days, months or years – measured in Megawatt-Hours (MWh)
  Example – a 100 MW power plant that generates at full power for 10 hours will produce 1,000 MWh

## Slide 26: Power Plant Metric - Capacity Factor
A power plant’s ‘capacity factor’ is a measure of how much energy (in MWh) it generates during the period of time being examined.
Capacity factor is given as a % - the plant’s actual generation (in MWh) in the period divided by the power it would have generated if it had operated at full power for all hours.
  Example – a power plant with a full power rating of 100 MW operates at only 50 MW for all of the hours of the period – its capacity factor is 50%.
  The amount of power generated by a plant will change (perhaps frequently) in response to plant outages, equipment problems or economic factors.
  The higher the capacity factor, the better.

## Slide 27: Capacity Factors - a Tale of Two Power Plants at the Same Site

## Slide 28: Power Plant Metric - Heat Rate
A power plant’s ‘heat rate’ measures how efficiently the plant burns fuel – the more efficiently the plant burns fuel, the less fuel it needs, and, consequently, the lower its fuel costs.
Heat rate is measured in British Thermal Units (btu) – energy input from fuel - per kilowatt-hour of electricity generated – btu/kwh
  The lower the heat rate, the better – this means it requires less energy input from the fuel to produce an average kwh of electricity.

## Slide 29: Illustrative Power Plant Heat Rates

## Slide 30: Fuel or Generation Mix – New England in 2013

## Slide 31: Where Can You Find Information about Power Plant Operations and Costs
Investor-owned companies (both regulated utilities and merchant) - Form 10-K annual filings to U.S. Securities and Exchange Commission.
Regulated investor-owned utilities – Form 1 annual filings to state utility commission and/or Federal Energy Regulatory Commission.
Data filed by plant owners with the U.S. Energy Information Administration of the Department of Energy – especially Forms 860, 861, 923.
Public power utilities and electric membership cooperatives – Ask nicely, find a friendly board member to ask for info, file Freedom of Information Act requests (FOIA) requests.
Ask IEEFA or Synapse Energy Economics.

## Slide 32
Thank you!!
Contact:
David Schlissel: david@schlissel-technical.com
Cathy Kunkel: ckunkel@ieefa.org